Augmented Spark Gap Ignite	r For Propellants

07 January, 2012

This is a schematic, parts list and description of a DC augmented spark gap ignition system for firearm propellants which is capable of igniting all types of propellants when used with a breech-plug type igniter as described elsewhere.

WARNING!! This circuit produces high voltages and currents which can shock, burn or even cause sudden death. Its construction should not be undertaken by anyone who is not familiar with the safety procedures required for working with such circuits.

Part		Descr							*Mouser Part Number

R1		5W 200Ω Ohmite wire-wound resistor		588-95J200E

R2		100K 1/4W Carbon resistor				791-RC1/4-104JB

R3		1K 1/4W Carbon resistor				791-RC1/4-101JB

R4		100Ω 1/4W Carbon resistor				791-RC1/4-100JB

R5		2 MΩ 1/4W Carbon resistor				791-RC1/4-205JB

C1		120 μfd 330V Capacitor See note 1

C2		0.068  μfd 630V Vishay pulse capacitor		594-2222-383-20683

D1		3000V  .25A diode 					625-GP02-30-E3

BR1		Four D1s in bridge configuration

SCR		800V  8A SCR					576-S8008L

CCFL		TDK CXA-L10A Inverter See note 2			810-CXA-L10L

T1		Pulse transformer See note 3

Batt		CR123 3V Lithium Cell (or rechargeable)

- Mouser Electronics (http://www.mouser.com) can supply most components.

Note 1: Obtain from disposable camera flash units. Many can be found on eBay or from electronic surplus houses.

Note 2: There are two modifications required. First, the output must be floated from the input. There is a wire jumper on the side marked 'GND' which must be removed. See photo below

Second, the output must be taken from directly across the secondary transformer windings, not from the output capacitors. This can be done by either bridging the capacitor or by wiring directly to the transformer.

Note 3: The pulse transformer was made by winding a primary and secondary over a plastic bobbin containing a 10mm ferrite rod (look in eBay). I designed the custom bobbin, which you can either machine from acetal or (even better) have it 3D-printed by Shapeways (http://www.shapeways.com). To get this printed, download the file and then upload it to Shapeways. They will print it and send it to you for a nominal fee.

The primary is wound with five layers of #30 enameled wire, with each layer being epoxied and separated by either one thickness of  one mil Mylar or two thicknesses of standard weight paper. The wire ends should be soldered to the output leads and then buried into the channels in the bobbin. The secondary is then covered and epoxied with either two layers of Mylar or four layers of paper, and then the secondary is wound with eight spaced turns of #24 enameled wire.